## Slide 1
AA
AF
11
22
33
44
66
77
88
99
10
20
55
BA
Frame Aligner Verification
Specification-driven verification of a byte-stream frame aligner
8 DUT defects, 3 critical / high
Corrected RTL: 0 spec violations
100 % functional coverage
Yakir Aqua · Verification plan, results and bug report · revised edition
Notes: Revised edition of the verification plan. The environment was rebuilt around an independent specification model; the delivered RTL is unchanged and was re-verified.

## Slide 2
0x01
Results at a glance
Frame Aligner Verification
2
8
DUT defects
3 critical / high; DUT-02 and DUT-03 had been filed as "spec gaps"
0
unexplained mismatches
every one of 255 spec violations on the delivered RTL is attributed to a known defect
100 %
functional coverage
14 spec-feature coverpoints, every cover property hit
910 k
fuzzed cycles cross-checked
corrected RTL = 3 independent spec models, 0 differences
Delivered RTL: TEST FAILED, 255 spec violations and 214 of 3,555 test-plan checkpoints failed, 0 unexplained. Corrected RTL: TEST PASSED, 0 violations, all checkpoints, 0 assertion failures.

## Slide 3
0x02
The design under test
One byte per clock; a frame is a 16-bit header (LSB first) and 10 payload bytes, back to back
Frame Aligner Verification
3
Frame format and fr_byte_position
AA
0
AF
1
P0
2
P1
3
P2
4
P3
5
P4
6
P5
7
P6
8
P7
9
P8
10
P9
11
HEAD_1 = 0xAFAA (AA then AF)
HEAD_2 = 0xBA55 (55 then BA)
Align
after 3 consecutive frames with a correct header: frame_detect = 1
Lose
after 4 frames without a header (48 header-less bytes): frame_detect = 0
Track
fr_byte_position = index 0..11 of the last byte (registered output)
PHY RX
frame_aligner
FR_IDLE
FR_HLSB
FR_HMSB
FR_DATA
legal_frame_counter[1:0]
na_byte_counter[5:0]
header_lsb_samp[7:0]
rx_data[7:0]
frame_detect fr_byte_position[3:0]
clk, reset (async)

## Slide 4
0x03
From the specification to seven checkable rules
The text, the design slides and the RTL disagree in places; the verification fixes one interpretation
Frame Aligner Verification
4
R1
Header = LSB immediately followed by its MSB: AA AF or 55 BA
text p.3, p.5
R2
While hunting, every byte is examined; a wrong MSB that is itself an LSB starts a new candidate. No header in the stream is missed
text p.3
R3
After a header the next 10 bytes are payload and are not examined
design slides (FSM)
R4
frame_detect rises one byte after the 3rd consecutive header (payload byte 0)
text p.6, waveform 1
R5
frame_detect falls on the 48th consecutive byte that is not part of a validated header
text p.6, register table
R6
fr_byte_position = index of the byte just consumed (0..11); 0 while hunting
port table, waveform 1
R7
Asynchronous reset: outputs 0, hunting restarts
port table
Implemented three times, independently: SV reference model, a causal Python model and an offline frame parser. They agree on every cycle.

## Slide 5
0x04
Why the environment was rebuilt
The original bench could not fail: its model was a copy of the RTL, and mismatches were fixed in the scoreboard
Frame Aligner Verification
5
 | Original environment | New environment
Reference | copy of the RTL (and even that one byte early) | spec rules R1-R7, cross-checked by two Python models
Mismatch policy | "correct the scoreboard" | attribute to a known defect, or flag as UNEXPLAINED
Expected outcomes | not checked | 3,555 checkpoints at exact byte positions
Stimulus | X bytes; 117 of 917 items never driven; preconditions shuffled away | 2-state; everything driven; every scenario starts from reset
Timing | program-block dependent; reset released on a clock edge | clocking blocks; reset on the falling edge
Assertions | 3 of 3 vacuous or false; failures not counted | 25 rule-based assertions, counted; non-vacuity proven
Coverage | reachable illegal bins, unreachable bins, no spec features | 14 spec-feature coverpoints, closed at 100 %

## Slide 6
0x05
Verification architecture
Class-based SystemVerilog, race-free clocking blocks, assertions bound into the DUT
Frame Aligner Verification
6
generator
+ 27 scenarios
driver
DUT
frame_aligner
+ fa_spec_sva (14)
+ fa_whitebox_sva (11)
monitor_in /
monitor_out
drv_cb
(+1 ns)
mon_cb
(#1step)
scoreboard
spec model
R1-R7, knobs off
DUT model
known defects on
checkpoints
test-plan outcomes
coverage
14 coverpoints
checkpoints
Monitors are numbered sample by sample; the scoreboard proves lock-step and compares outputs(k) with the model after byte k-1.

## Slide 7
0x06
Every mismatch is triaged, not "fixed"
Two instances of the same specification model: one pure, one with the delivered design's defects switched on
Frame Aligner Verification
7
DUT outputs
at cycle k
equal to the
spec model?
equal to the
DUT model?
no
MATCH
yes
KNOWN DEFECT
attributed to
DUT-0x
yes
UNEXPLAINED
new problem
no
Known defect: the knob that fired in the DUT model names the defect; the spec model is then re-synchronised to the DUT's path, so each occurrence is reported once, with no cascade.
+MODEL=dut: the same bench becomes a regression bench for the delivered RTL and fails only on NEW behaviour.
Result on the delivered RTL: 255 spec violations, 0 unexplained.

## Slide 8
0x07
Three independent oracles, three independent models
Frame Aligner Verification
8
1
Reference model
every byte, every cycle
cycle-accurate compare of frame_detect and fr_byte_position against R1-R7
2
Checkpoints
3,555 expected outcomes
the test plan's "expected outcome" column, checked at the exact byte (e.g. "aligned after 47 header-less bytes, lost on the 48th")
3
Assertions
14 black-box + 11 white-box
spec rules on the ports; FSM and counter checks inside the DUT catch latent defects the ports never show
Differential fuzzing (scripts/fuzz_rtl.py): 6 000 streams, 910 k cycles
corrected RTL = SV spec model = Python causal model = independent frame parser: 0 differences
delivered RTL = bug-emulating model: 0 differences (every deviation is DUT-01, 02 or 03)
delivered RTL vs. specification: 13 % of all cycles wrong on stress traffic

## Slide 9
0x08
Test plan (1/2)
Every scenario starts from reset and checks its expected outcome at exact bytes (checkpoints)
Frame Aligner Verification
9
ID | +TEST= | Stimulus | Expected (spec) | Exposes
TP01 | spec_suggested | 5xHEAD_1, 4 illegal, 5xHEAD_2 (spec p.23) | aligned on frame 3; lost on the 48th byte | 
TP02 | mixed_headers | HEAD_1 / HEAD_2 in any mix | aligned after 3 frames | 
TP03 | swapped_header | AF AA / BA 55; 4 of them while aligned | never aligns; loss on the 48th byte | DUT-03
TP04 | inverted_header | bit-inverted and bit-reversed headers | never aligns | DUT-03
TP05 | lsb_ok_msb_bad | AA 01, 55 01, AA 00, 55 00, AA BA, 55 AF | position 0 after the rejected MSB | DUT-03
TP06 | lsb_bad_msb_ok | 0A AF, 05 BA | position 0, never aligns | 
TP07 | msb_in_payload | AF / BA bytes inside payloads | frame boundaries unchanged | 
TP08 | header_in_payload | headers at every payload offset | ignored (R3) | 
TP09 | restart_header | AA¦AA AF, 55¦55 BA, AA¦55 BA, 55¦AA AF, ... | header found; aligned after 3 frames | DUT-01
TP10 | loss_boundary | aligned, 44..48 header-less bytes, header | kept for <= 46, lost for >= 47 | DUT-02
TP11 | corrupted_frames | aligned, 1..4 corrupted frames | kept for <= 3, lost on byte 48 for 4 | DUT-03
TP12 | header_in_illegal | legacy illegal frames with inner headers | frame at the inner header | 
TP13 | frames_in_illegal | 3 frames inside a 49-byte illegal frame | aligned exactly on byte 29 | 
TP14 | header_soup | 49-byte frames of random header bytes | model-checked | DUT-01/03

## Slide 10
0x08
Test plan (2/2)
Every scenario starts from reset and checks its expected outcome at exact bytes (checkpoints)
Frame Aligner Verification
10
ID | +TEST= | Stimulus | Expected (spec) | Exposes
TP15 | lsb_at_payload_end | payload ends in AA / 55 / AA AF (aligned) | next header found | 
TP16 | long_valid_run | 10 consecutive frames | aligned; counter saturates | DUT-04
TP17 | long_garbage | 80 header-less bytes, re-align | lost on 48; counter saturates | DUT-05
TP18 | reset_every_phase | async reset in each phase, aligned or not | outputs 0; no header across reset | 
TP19 | false_lock_in_sync | corrupted header + header pattern in payload | locks on the false frame | DUT-07 demo
TP20 | consecutive_rule | V, 1 byte, V, V, V | aligned only after frame 4 | 
TP21 | header_across_items | ... AA ¦ AF ... across two items | recognised | 
TP22 | illegal_lengths | illegal frames of 2..49 bytes (aligned) | lost on exactly the 48th byte | 
TP23 | boundary | sweep 0..60 header-less bytes, +/- stray LSB | kept iff gap + prefix <= 46 | DUT-01/02
TP24 | loss_cause | 48th byte = rejected MSB / restart LSB | lost on that byte | DUT-01
TP25 | midstream_entry | start mid-stream; payloads end in 55 / AA | aligned after 3 frames | DUT-01
TP26 | error_then_lsb_payloads | 1 header error, then payloads ending in 55 | alignment kept | DUT-01
TP27 | slip_in_sync | 13-byte frames before / after alignment | hunting keeps alignment | DUT-07 demo
RND | random | 61 % valid, 18 % illegal, 8 % restart, 12 % gap, 2 % reset | model + assertions | all

## Slide 11
0x09
Spec-feature coverage and assertion results
Coverage is sampled from the reference model, so it measures behaviour, not raw signal values
Frame Aligner Verification
11
CP02 / CP03
every transition (hunt, LSB, reject, restart, frame) x aligned
CP06
every byte that can follow a header LSB
CP07
gap before a header while aligned: 0 .. 44, 45, 46 (last chance)
CP08
every kind of 48th byte: plain, LSB, rejected MSB, restart LSB
CP09
fr_byte_position 0..11 x frame_detect
CP11
asynchronous reset in every phase, aligned or not
CP12
header patterns inside payloads
100 % of 14 coverpoints (102 bins) in the regression; every cover property hit
Chart: Assertion failures on the delivered RTL (corrected RTL: 0)
| SPEC_POS1_AFTER_HEADER | SPEC_POS_INCREMENT | SPEC_SYNC_AFTER_3_FRAMES | SPEC_FD_FALL_AFTER_48 | SPEC_FD_FALL_WHILE_HUNTING | WB_DUT01_NO_LOST_LSB | WB_DUT02_NO_CLEAR_IN_FRAME | WB_DUT03_POS_RESET_ON_REJECT | WB_DUT04_LEGAL_NO_WRAP | WB_DUT05_NA_NO_WRAP
failures | 252 | 251 | 24 | 28 | 6 | 149 | 3 | 252 | 32 | 40

## Slide 12
DUT defects
The student's scoreboard mirrored the RTL, so these were either unseen or filed as "gaps in the spec".
DUT-01
Header LSB lost: legal streams never align
Critical
DUT-02
Alignment dropped on a valid header
High
DUT-07
No fly-wheel: slips never lose alignment
High (arch.)
DUT-03
Position 1 reported for a rejected header
Medium
DUT-04
Frame counter wraps 3 -> 0
Low (latent)
DUT-05
Byte counter wraps 63 -> 0
Low (latent)
DUT-08
X-optimistic header decode
Low
DUT-06
Coding issues (default, width, comments)
Info
Frame Aligner Verification
12

## Slide 13
DUT-01
Header LSB thrown away after a rejected MSB
Critical · extends the student's "LSB twice then MSB": it happens for all four LSB combinations
Frame Aligner Verification
13
Root cause
In FR_HLSB a wrong MSB always returns to FR_IDLE. If that byte is itself a header LSB (AA / 55) it is never examined, so its header is missed.
end else if (header_lsb_valid) begin // FIX DUT-01
legal_frame_counter_rst = 1'b1; fr_byte_position_rst = 1'b1;
na_byte_count_inc = 1'b1; next_state = FR_HLSB;
end

## Slide 14
DUT-01
Legal traffic is never aligned
Payload byte 9 = 0x55 (or 0xAA) looks like a header LSB; the real LSB rejects it and is thrown away, for every frame
Frame Aligner Verification
14
never
aligned: start-up in the middle of a legal stream whose payloads end in 0x55 (TP25: 20 of 20 checkpoints fail)
permanent
loss after one bit error in a header, if the following payloads end in 0x55 (TP26)
1 in 128
chance per bad frame of losing alignment after only 3 bad frames (random payload)

## Slide 15
DUT-02
Alignment dropped on a valid header
High · the student saw "last chance is a header at byte 45" and filed it as a spec gap
Frame Aligner Verification
15
Root cause
the header LSB is counted as a non-aligned byte (46 -> 47)
the clear (na_byte_counter == 47) is not qualified: the valid MSB clears frame_detect
the whole valid frame is received with frame_detect = 0; outage lasts 3 frames
gap | spec | delivered RTL
<= 45 | kept | kept
46 | kept | LOST
>= 47 | lost | lost
Fix: clear only when the consumed byte is itself counted: na_byte_count_inc && na_byte_counter == 47

## Slide 16
DUT-03
Position reported for a rejected header
Medium · the student noted the one-cycle "1" and filed it as a spec gap
Frame Aligner Verification
16
What happens
after AA 01 the output says "header MSB" (position 1) although no frame exists
every other hunting byte reports 0, so a consumer sees a phantom header
the FSM slide omits the position reset on the HLSB -> IDLE arc too
Fix: fr_byte_position_rst = 1 on the reject arc. Caught by SPEC_POS1_AFTER_HEADER, SPEC_POS_INCREMENT and WB_DUT03_POS_RESET_ON_REJECT.

## Slide 17
DUT-04
Latent and hygiene defects
Invisible on the ports today; caught at the root cause by white-box assertions and lint
Frame Aligner Verification
17
DUT-04
legal_frame_counter wraps 3 -> 0 on the 4th frame (above). Caught by WB_DUT04_LEGAL_NO_WRAP. Fix: saturate.
DUT-05
na_byte_counter wraps 63 -> 0 on long header-less streams. Caught by WB_DUT05_NA_NO_WRAP. Fix: saturate.
DUT-06
no next_state default; 4-bit vs 8'd10 compare; wrong comments. The corrected RTL is verilator -Wall clean.
DUT-08
X on rx_data is silently decoded as "not a header" in RTL, but not in gates. TB_IN_KNOWN forbids X stimulus.

## Slide 18
DUT-07
No fly-wheel: slips never lose alignment
High (architecture) · spec text: out of alignment after four frames without the EXPECTED header
Frame Aligner Verification
18
13-byte frames: every header one byte late, and frame_detect stays 1 forever. The same stream never aligns from reset (hysteresis).
Tracking stops: after one bad header, fr_byte_position is 0 for a whole frame while frame_detect = 1; a header pattern in a payload re-bases the frame (false lock).
Proposed fix: while aligned, count 0..11 freely, check headers only at the expected position, and declare out-of-frame after 4 bad frames. Hunt byte by byte only while not aligned.

## Slide 19
0x0A
Issues in the specification itself
To be clarified with the designer; each affects what "correct" means
Frame Aligner Verification
19
SPEC-01
Output data interface (header + payload forwarding) is specified but not implemented
SPEC-02
Text: loss after 4 frames without the expected header. Design slides: 48 hunting bytes. Leads to DUT-07
SPEC-03
Waveform 2 is one clock late against the FSM slide and the RTL; waveform 1 starts in an unreachable state
SPEC-04
fr_byte_position is undefined outside a frame and has no valid qualifier (0 = LSB and 0 = not aligned)
SPEC-05
Name mismatches: fr_is_aligned / frame_detect, na_frame_counter / na_byte_counter, Valid_h2 missing
SPEC-06
The 48th header-less byte is a header LSB: counted (register table) or not (look-ahead)? The RTL violates both

## Slide 20
0x0B
Defects in the original testbench
Why the original run looked clean although the design is not
Frame Aligner Verification
20
12.8 %
of the queued stimulus never driven (117 of 917 items): end of test compared transactions with repeat_count
1 byte
early: the "copied" model sets and clears frame_detect one byte before the RTL, so no clean run was possible
102
false assertion failures per run from one legacy property; the other two are vacuous or always fail
TB-01
model copied from the RTL; mismatches fixed in the scoreboard
TB-04
5 directed tests drive X (new[N] on a 4-state array, 8'hxA)
TB-05
tests shuffled: preconditions not met, tests spill into the next one
TB-07
coverage: reachable illegal bins, unreachable bins, no spec features
TB-08
sampling depends on program-block scheduling; reset on a clock edge
TB-09
2-state scoreboard turns X/Z into 0
TB-10
build order wrong; bind by instance name not elaborated
TB-11
out-of-bounds writes, misleading "illegal" frames, no seed control

## Slide 21
0x0C
Regression results
make -C sim regress: every run is checked against its EXPECTED outcome
Frame Aligner Verification
21
RTL | test | model | cycles | checkpoints | verdict | expected
corrected | directed | spec | 4,300 | 995 / 995 | PASS | PASS
corrected | boundary sweep | spec | 9,701 | 2,560 / 2,560 | PASS | PASS
corrected | random | spec | 6,485 | - | PASS | PASS
corrected | regression | spec | 20,985 | 3,555 / 3,555 | PASS | PASS, cov 100.0 %
delivered | regression | DUT | 20,985 | tolerated | PASS | PASS (no new behaviour)
delivered | regression | spec | 20,985 | 3,341 / 3,555 | FAIL | FAIL, 0 unexplained
Chart: Spec violations attributed per defect
| DUT-01 | DUT-02 | DUT-03
delivered RTL | 149 | 3 | 252
corrected RTL | 0 | 0 | 0
RTL untouched: hash of the annotated DUT = hash of the delivered dut.sv
The corrected RTL is verilator -Wall clean
Differential fuzzing: 0 differences between the corrected RTL and the three specification models

## Slide 22
Conclusions
The design is not bug-free. Its header search can miss every header of a legal stream (DUT-01) and drops alignment on a valid header (DUT-02).
A scoreboard that copies the RTL cannot find design bugs. The spec model with defect triage found all of them, with 0 unexplained mismatches.
Expected outcomes must be executable. 3,555 checkpoints turn the test plan into checks.
Evidence, not assumption. Three independent models agree; the corrected RTL passes everything.
Next steps
Designer to accept DUT-01..06 fixes (rtl/frame_aligner_fixed.sv)
Decide on the fly-wheel (DUT-07) and resolve SPEC-02/-06
Add the output data interface (SPEC-01)
Run the bench on a commercial simulator to merge native covergroups
Formal proof of R1-R7 on the corrected RTL
Frame Aligner Verification
22

## Slide 23
0x0D
Appendix: how to run
Verilator >= 5.030 with z3; Python 3; Icarus Verilog for scripts/
Frame Aligner Verification
23
cd sim
make sim DUT=fixed # corrected RTL -> TEST PASSED
make sim DUT=orig # delivered RTL -> TEST FAILED, defects listed
make sim DUT=orig MODEL=dut # regression mode -> only new behaviour fails
make sim DUT=orig TEST=restart_header VERBOSITY=2
make sim DUT=orig TEST=loss_boundary WAVES=1 # waves.vcd
make regress # full matrix, expected outcomes
python3 ../scripts/fuzz_rtl.py # differential fuzzing (Icarus)
python3 ../scripts/plot_waves.py # regenerate the figures
Documents: docs/BUG_REPORT.md (every defect, reproduction, fix) · docs/VERIFICATION_PLAN.md (rules, test plan, coverage, assertions, results)